• Methods: Since the focus of the study is on physical modeling, it would make sense to start presenting the MUSC laboratory (section 2.2) rather than the numerical method used for comparison (section 2.1).

It'is done in the corrected version

Furthermore, when presenting the MUSC laboratory it would be helpful for readers to mention limitations which are expected. For example, it is known that ultrasonic transducers are resonant and narrow-band due to the physical properties of these devices. Also, the transducers are in general large compared to the minimum wavelength of the simulation, thus can impose directivity effects. Some of these effects have been studied by Fran ̧cois Bretaudeau et al. (2011) already, but it would be great to further mention and justify the selected frequency-bandwidths of 20 - 200 kHz and 300 - 800 kHz.

These remarks are tackled in the corrected version (in part 2. Methods - theadded text is written in Magenta color) in 3 separated parts as following :

1) For example, it is known that ultrasonic transducers are resonant and narrow-band due to the physical properties of these devices.

Piezzo-electrics components are indeed resonant. One of the difficulty to avoid the resonnant effect is the impedance adaptation of the transducer to the propagating medium. However, in MUSC, we use tranducers who have been built with well-adapted shape, backing element and suited material for the contact to the medium, in order to be adapted to the impedence of the material that we use, as much as possible (for exemple, they are not adapted to alluminium blocks). That is specially the case of those adapted to a central frequency of 100 KHz in the paper. In the case of the higher frequency one (not used in the tests described here), a conical adaptator in resin between the transducer and the model allow to weak the resonant effect. This aspect is already described in (Bretaudeau et al, 2011) and, to our mind, it should not be repeated with long developments in the present paper. However, it is recalled in the corrected version as recommended, at the end of the third paragraph. Moreover, even if the resonnant effect are avoided, the response of the transducer remains as a filtering effect to the electrical signal injected in input. This aspect is a critical point tackled in the present proposed article. For this reason, we complete the added sentence of the 3d paragraph by this aspect. The part added :

« The piezzo-electric transducers used are built to be adapted to the impedance of the resin model described in the next part. Thus the emitted signal, already presented in (Bretaudeau et al. 2011) is not resonant. However, the sensor response combined with the coupling effect to the model behaves as a filter for the source shape. This effect is a crucial point that has been firstly tackled in MUSC by (Bretaudeau et al. 2011) with an assumption of 2D propagation although in case of a punctual source. In the present paper, we propose to study further the impact of this source response on the data by taking into account the 3D effects of a punctual source and by simulating a 2D source line. Note that the transducer response and the coupling effect depend on the frequency of the emitted signal. We will tackle this frequency dependance by taking into account the entire waveform of the pulse . »

Concerning the narrow-band aspect, the following text has been added in the subsection « Characteristics of the scale models tested » :

« As shown on figure 2, even if the emission properties of a piezzo-electric transducer is narrow-band, the spectral bandwith of the pulse emitted by the piezzo-electric transducer is large enough to simulate a seismic pulse emitted by a hammer fall in subsurface media, through the scale ratio used in table 2. »

2) Also, the transducers are in general large compared to the minimum wavelength of the simulation, thus can impose directivity effects. Some of these effects have been studied by Fran ̧cois Bretaudeau et al. (2011) already, but it would be great to further mention
Precisions about this have been added in the corrected version in paragraph 4 through the following sentences :

« Actually, as explained in Bretaudeau et. al. 2011, classical piezzo-electrical transducers sizes are generally large compared to the emitted wavelength and provide a directional emission pattern whereas a hammer fall source used in subsurface field measurements behaves as a punctual impact and provides an omnidirectional emission pattern. For this reason, in the MUSC laboratory, two adapted sources have been tested in term of directivity pattern by (Bretaudeau et al.) who showed their capacity to simulate a thin piston effect. The first one, corresponding to the lower frequency band [20-200] is a commercial one with a small impact contact. The second one, corresponding tio the higher frequency band. ...

3) and justify the selected frequency-bandwidths of 20 - 200 kHz and 300 - 800 kHz.
It has been clarified in the corrected version through the following sentences whixh have been inserted in the 5th paragraph :

This two frequency bands have been chosen to allow both complying with the dimensional scale ratio shown in tables 1 and 2 and making easily the heterogeneities in the medium. That means : the heterogeneities should be not too small (1mm of minimal size) and the total model size should not be too big or too heavy (1m2 and 270 Kg max) for the supporting table. For simulating classical dimensions in the subsurface domain, we use preferentially the low frequency band which allows a dominant wavelength (at 100kHz) about 13 mm for the Rayleigh waves and 28 mm for the P waves, by taking into account the velocity in the models described below. The scale ratio principles are used as follows

Concerning the following remark :

Also, it would be great to evaluate the precision achieved of the measurements in the MUSC laboratory. For example, the precision of the positioning of the receiver position is stated as ±10μm which for a shortest wavelength of 1mm amounts to a precision of 1%. So does the vertical offset measurement by a laser beam with a 20μm diameter, thus the measurement is not exactly a point measurement but an average over a small surface fraction. One could briefly present for the chosen setups what error of the measurement would be expected. Since this is one of the advantages of laboratory settings, you could put error bars on the traces.

The following text has been added in the subsection « Characteristics of the scale models tested » :

« The laser beam diameter is 20μm large. In the presented study, typical of experimentations in MUSC, the dominant wavelength (at 100kHz) equals about 13 mm for the Rayleigh waves and 28 mm for the P waves . Thus, the laser beam respectively equals lamda/650 and lamda/1400. At the field scale, and following the rules in table 1, those corresponds to a measurement surfaces of 20 mm and 2 mm respectively. These dimensions are lower or equivalent to the possibilities available by geophones holds. Thus, at the laboratory scale in MUSC, the measurement accuracy in term of the size of the recording surface is respected »

In parallel, the position accuracy of the receiving system is 10μm. This value is lower to the focal beam. It corresponds to the center position of the laser beam, which is 20μm large. In practice, the incremental displacement between two receivers positions used here equals mm. It is higher than the focal beam size

Concerning the following remark :

The same consideration also holds for the ringing of the transducers which will likely look different at different central frequencies. One could present the ringing for different central frequencies of the source, to better highlight in which frequency regime the transducers affect measurements and need to be treated more carefully as is then done in the following of this study.

The frequancial effects of the transducer is tackled thorugh the entire waveform, as added in the modified version (see the corrected part to answer to your comment 1) ) of the Methods part above.